## Slide 1: Project 9: EKF-based Localization with LRF
Presentation 2:
Progress, Theory and Outlook
Notes: Last but hopefully not least, second presentation about our project. Project number 9: Extended Kalman Filter based Localization using a Laser Range Finder

## Slide 2: Outline
Progress
  Robot
  Theory
Outlook
Questions
Notes: What are the topics I am going to talk about?
First up is the progress we were able to achieve in the last 3 weeks. On the one hand robot based progress and on the other hand also progress in understanding the EKF.
This is followed by a short outlook on what we aim for in the next 3 weeks and then I am going to end the presentation with some question.

## Slide 3: Outline
Progress
  Robot
  Theory
Outlook
Questions
Notes: So let‘s do not waste any time and get started.

## Slide 4: Progress
Matching
Prediction
Update
General idea about our task, ROS and the EKF
Mapping the room
Combining pre-acquired map with the mapped room
Building autonomy
Optimizing for the problem
EKF
Solution Approach:
3 weeks ago:
Notes: This is a brief summary of what Thiago presented to you last time and what basically was our position at that time. We had a general idea about our task, about ROS and about the EKF. We used this extremly superficial model to sum up the EKF. Additionally we showed a 4 step solution approach, which first step was to map the room. So this was where we started 3 weeks ago. What do we have now?

## Slide 5: Robot (1)
First step of the solution approach
Working ROS Environment
  Communication with Robot (ROSARIA)
  LRF & Odometry connected to RVIZ
Remote control robot with keyboard from second laptop
First version of a map of the 5th floor (slam_gmapping)
Today:
Notes: Today we have a working ROS environment, which includes the communication with the robot, using the Rosaria package. We are also able to connect the LRF and the Odometry to RVIZ.
We can control the robot by using the keyboard and even use a second laptop to remote control the robot.
Yesterday we were able to obtain a first version of a map of the 5th floor corridor using the slam_gmapping package. So we were able to finish the first step of our formulated solution approach.
In order to prove these things we prepared a video, that we recorder yesterday.

## Slide 6: Robot (2)
VIDEOS
Notes: Goncalo remote controlling the robot
LRF on the front side. Remote controlling does not only look cool, it is also useful for mapping corners.
Here you can see the mapping in the RVIZ This part obviously also is a lot of fun.

## Slide 7: Robot (3)
Notes: So far we mapped the corridor 4 times. We used different settings and methods for this. Results are showen here.
Good: Elevator part. Class room, some straight parts
Bad: Straights are not straight  Closing the map does not work

## Slide 8: Theory (1)
Prediction
Observations
World Map
Matching
Odometry
Observation model
Update
Based on the EKF localization slides
Non linear dynamics:
Approximation by linearization around last state estimate
Linearization has to be a good approximation to be valid
Otherwise the EKF may even diverge
Notes: Enought to robot progress, let‘s continue with progress in understanding the EKF This is a basic but more detailed in comparison to the last time, model of the EKF. EKF is used for systems with non linear dynamics. State in next time step equals f, which depends state and input) + process noise. Observation equals h + observation noise.
The non linear dynamics cause non gaussian pdf., which makes it hard to determine the mean and the variance. That‘s why a linearization is used as an approximation.
In which parts is this linearization used? f: nonlinear state function
h: nonlinear observation function
w: process noise (white & gaussian)
v: measurement noise (white & gaussian)

## Slide 9: Theory (1)
Prediction
Observations
World Map
Matching
Odometry
Observation model
Update
Based on the EKF localization slides
Non linear dynamics:
Approximation by linearization around last state estimate
Linearization has to be a good approximation to be valid
Otherwise the EKF may even diverge
Linear models
Notes: In the prediction block
Linearized system dynamics are used for the odometry prediction
In the observation model linearized observation dynamics are used

## Slide 10: Theory (2)
Prediction
Observations
World Map
Matching
Odometry
Observation model
Update
Based on the EKF localization slides
Consider the last filtered state estimate
Linearize the system dynamics, around
Apply prediction step on linearized dynamics to obtain and
Linearize the observation dynamics, around to obtain
Notes: Let’s have a look on how the EKF works. 1. Consider the last filtered state estimate As the prediction used the linearized model, giving the mean and the variance is enough to get a gaussian probability density function
2. Linearize the system dynamics, around
3. Apply the prediction step of the Kalman filter to the linearized system dynamics
t and
4. Linearize the observation dynamics, around and use this to get a observation prediction
1. Consider the last filtered state estimate 𝑥 ̂(𝑘│𝑘) As prediction is linearized model giving the mean and the covariance is enough to get a gaussian probability density function
2. Linearize the system dynamics, 𝑥_(𝑘+1)=𝑓(𝑥_𝑘,𝑢_𝑘 )+𝑤_𝑘 around 𝑥 ̂(𝑘│𝑘)
3. Apply the prediction step of the Kalman filter to the linearized system dynamics
just obtained, yielding 𝑥 ̂(𝑘+1│𝑘)and 〖 Σ〗_𝑥 (𝑘+1|𝑘)
4. Linearize the observation dynamics, 𝑧_𝑘=ℎ(𝑥_𝑘 )+𝑣_𝑘 around 𝑥 ̂(𝑘+1│𝑘),
5. Apply the filtering or update cycle of the Kalman filter to the linearized
observation dynamics, yielding 𝑥 ̂(𝑘+1│𝑘+1)𝑎𝑛𝑑 Σ_𝑥 (𝑘+1|𝑘+1)

## Slide 11: Theory (3)
Prediction
Observations
World Map
Matching
Odometry
Observation model
Update
Based on the EKF localization slides
Try to match the real observation with the predicted one
Update the current state
Notes: 5.
6.
That is the general model. For our case we can change two small things

## Slide 12: Theory (4)
Prediction
LRF
Map
Matching
Odometry
Observation model
Update
Based on the EKF localization slides
Notes: On the one hand we know that the observation will be made by our LRF. And on the other hand the world map is our pre acquired map

## Slide 13: Outline
Progress
  Robot
  Theory
Outlook
Questions
Notes: So how will we use this knowledge and continue our work on the project

## Slide 14: Outlook (1)
Prediction
LRF
Map
Matching
Odometry
Observation model
Update
Based on the EKF localization slides
Improve!
Notes: You can see, I really like this model.
This time it shows what we have right now. We are able to get the raw data from the LRF and we are also able to obtain the map, which, let‘s be honest, we still need to improve massively.
So what do we need to do next? Ît is as simple as this: We need to implement the EKF

## Slide 15: Outlook (2)
Implementing the EKF
  Odometry prediction
  Observation model
  Matching
  Update
Prediction
LRF
Map
Matching
Odometry
Observation model
Update
Based on the EKF localization slides
Notes: This includes the 4 parts: odometry prediction, the observation model, the matching and the updating.
Some of these parts will probably be harder than others. But in difference to the last 3 weeks, we hope, that we can parallelize some of the work.
In three weeks we will tell you how good that idea worked out.

## Slide 16: Questions
Will the wheels be recalibrated?
Notes: As we just finished the mapping part yesterday, we honestly dont have too many questions on the upcoming parts. The only thing we bothered about obviously was the not straight driving robots.