## Slide 1: Extended Kalman Filter

## Slide 2
The Extended Kalman Filter is an algorithm in which we can achieve relative and absolute localization through a recursive process with three stages:
Matching/Filtering
Update
Prediction

## Slide 3: Matching
Inputs -> Observations from the environment
It is the stage that occurs after a prediction. In this stage of the algorithm it is necessary to match the prediction with the observations at the new state in order to avoid miscalculations.
If the the Matching is successful then the state and world map is updtated.
Notes: After the prediction stage of the algorithm it is necessary to match the prediction with the observations at the new state in order to avoid miscalculations. We therefore do a matching of the observations we predicted and the real world observations. All this is necessary to avoid EKF divergence, ignore outlier observations and to ignore erroneous or inexistent predictions.
If a matching fails then we go to the "detection and correction of bias", here we calculate a new state vector and a new observation vector and then match the observation vector with the real world observation to see if it a correct prediction.

## Slide 4: Update
The EKF updates it knowledge of the world map with the obtained observations and also its new position.

## Slide 5: Prediction
The prediction is made in two steps using a combination of two prediction estimates, the Odometry predicted estimate and then the Observation Model estimate which relates to the world map.
Notes: The world Map is a group of Points and Line segments constituing landmarks.
The Observation Model creats a mapping of the observation using the information received from the sensor model. Each sensor model has characteristics such as spatial perception and effective beawidth which give us the limits of our observations.

## Slide 6: Limitations and disadvantages
The EKF depends on it’s previous knowledge of the environment in order to make predictions.
If the initial estimate of the state is wrong, or if the process is modeled incorrectly, the filter may quickly diverge, owing to its linearization.
Without the addition of “stabilising noise” the covariance matrix tends to underestimate the true covariance matrix therefore risking to become inconsistent.
Notes: Disadvantages of the extended Kalman filter:
Unlike its linear counterpart, the extended Kalman filter in general is not an optimal estimator (of course it is optimal if the measurement and the state transition model are both linear, as in that case the extended Kalman filter is identical to the regular one). In addition, if the initial estimate of the state is wrong, or if the process is modeled incorrectly, the filter may quickly diverge, owing to its linearization. Another problem with the extended Kalman filter is that the estimated covariance matrix tends to underestimate the true covariance matrix and therefore risks becoming inconsistent in the statistical sense without the addition of "stabilising noise".
Having stated this, the extended Kalman filter can give reasonable performance, and is arguably the de facto standard in navigation systems and GPS.